## Slide 1: Clarification on Maritime Casualty Reporting Requirements
NAVIGATION AND VESSEL INSPECTION CIRCULAR NO. 01-15
Published July 21, 2015

## Slide 2: Background
Concern that USCG field commands had varying interpretations regarding what types of marine incidents should be reported and investigated.
A draft of the new NVIC was originally published for comment in the Federal Register in January 2014.
The majority of the comments received from multiple industry segments and organizations made it clear that more detail was needed for specific types of marine casualties.

## Slide 3: NVIC 01-15 July 21, 2015
circular is intended to serve as a common framework of understanding for both Coast Guard and maritime industry personnel
USCG will utilize the circular when conducting preliminary investigations to determine whether a reportable marine casualty has occurred.

## Slide 4: Maritime Industry Responsibility
the owner, agent, master, operator, or person in charge must determine whether an occurrence meets the criteria for notifying the Coast Guard.
If there is any doubt whether an occurrence is a reportable marine casualty event, the USCG strongly encourages the responsible industry parties to contact the Officer in Charge, Marine Investigations for guidance.

## Slide 5: Hazardous Conditions must still be reported
To be reported, incident must qualify as a “Marine casualty or accident” under 46 CFR 4.03-1 and also satisfy criteria in 4.05-1. However, a marine casualty or accident that qualifies as a hazardous condition under 33 CFR §160.216 must be disclosed to the USCG even if it is not reportable under 4.05-1.
33 CFR 160.202: Hazardous Condition means any condition that may adversely affect the safety of any vessel, bridge, structure, or shore area or the environmental quality of any port, harbor, or navigable waterway of the United States. It may, but need not, involve collision, allision, fire, explosion, grounding, leaking, damage, injury or illness of a person aboard, or manning-shortage.

## Slide 6: Hazardous Conditions must still be reported
Falls overboard that do not result in injury or death –Unintentional or unauthorized falls overboard that create a hazard (e.g., a vessel has to turnaround in a congested waterway to recover an individual or the individual in the water narrowly misses being struck by other vessel traffic) should still be immediately reported as a hazardous condition.

## Slide 7: Hazardous Conditions must still be reported
“Bump and Go” Groundings – “Bump and go” groundings are occurrences where the involved vessel master or licensed mate on watch attests that the grounding (including grounded barges under the control of a towing vessel) was only momentary (e.g., reversing engines frees the grounded vessel on the first attempt, no assist vessel is needed to free the vessel, all towing connections remain intact) and that the grounding did not result in any other marine casualty criteria being met.
Not reportable under 46 CFR 4.05-1.
Initial notifications of “bump and go” groundings must still be made to the appropriate Coast Guard Command Center as a hazardous condition per 33 CFR Part 160.216.

## Slide 8: Timing and manner of notification
46 CFR 4.05(a): Immediately after the addressing of resultant safety concerns, the owner, agent, master, operator, or person in charge, shall notify the nearest Sector Office, Marine Inspection Office or Coast Guard Group Office—
Guidance: Immediately – Means as soon as reasonably practicable without delay. The Coast Guard should consider delays in reporting caused by the need to address resultant safety concerns, such as responding to an emergency situation, to be valid. However, the responsible parties involved in a marine casualty must make all efforts to notify the Coast Guard quickly.

## Slide 9: Examples of potential non-compliance with immediate notification
A crew member on a passenger vessel slips and breaks an arm during an excursion. The master fails to report the incident until completing a 40- minute transit back to port. When the Coast Guard IOs arrive on scene several witnesses have departed the vessel, impeding the ability to conduct an investigation.
A tank vessel loses all propulsion after switching to low sulfur fuel upon entering a North American Emission Control Area. The vessel’s engineers are able to troubleshoot the problem at sea and the vessel proceeds to its berth. The master of the vessel delays reporting the incident to the Coast Guard until the vessel is safely moored at the dock.

## Slide 10: Guidance: Notification
It is preferred that the notification be made to the Command Center of the Coast Guard Sector in whose area of responsibility the marine casualty occurs
A Coast Guard acknowledged phone or marine radio call for Coast Guard assistance meets the requirement to immediately notify.
33 CFR 160.216 “hazardous condition” reports also satisfy the immediate notification requirement for marine casualties but not the CG-2692 requirement (if one exists).

## Slide 11: What triggers the notification requirement

## Slide 12: 46 CFR 4.05-1(a)(1): An unintended grounding, or an unintended strike of (allision with) a bridge.
any situation where the vessel is unintentionally brought or placed on the ground, historically identified as being “ground” beneath the water line (e.g., sea floor, riverbed, silt, or rocks) except in circumstances where the grounding can be classified as a “bump and go” grounding.
Exception for “Bump and Go” Groundings – must be “only momentary” and not resulting in any other reportable event.
But initial notifications of “bump and go” groundings must still be made to the appropriate Coast Guard Command Center as a hazardous condition per 33 CFR Part 160.216.

## Slide 13: 46 CFR 4.05-1(a)(1): An unintended grounding, or an unintended strike of (allision with) a bridge.
It does not matter whether the unintended strike (allision) resulted in any damage, pollution, or injuries, because a strike (allision) with a bridge is in itself a reportable marine casualty.
Bridge is defined very broadly: a structure erected across navigable waters of the United States, including all integral elements of the overall structure, approaches, and appurtenances.

## Slide 14: 46 CFR 4.05-1(a)(2): An intended grounding, or an intended strike of a bridge, that creates a hazard to navigation, the environment, or the safety of a vessel, or that meets any criterion of paragraphs (a) (3) through (8)
A grounding is considered “intended” if it is a controlled, intentional maneuver to, among other things, hold position to adjust cargo, offload passengers, and/or hold position to allow other traffic to safely transit.
A strike (lay-up or landing) of a bridge is considered “intended” if it is a controlled, intentional maneuver to, among other things, assist, guide or walk a vessel through the bridge or hold position using the bridge or its protective fendering system.

## Slide 15: 46 CFR 4.05-1(a)(2): An intended grounding, or an intended strike of a bridge, that creates a hazard to navigation, the environment, or the safety of a vessel, or that meets any criterion of paragraphs (a) (3) through (8)
Due to the potential of compromising the integrity of the bridge or its protective systems, all intended strikes (allisions) that cause any damage, however minimal, shall be reported to the local USCG Sector Command Center as a hazardous condition under 33 CFR 160.216.
However, these incidents do not require a written CG-2692 unless they create a hazard to navigation, the environment, or the safety of a vessel, or meet other casualty reporting criteria under 46 CFR 4.05-1(a)(3)-(8).

## Slide 16: 46 CFR 4.05-1(a)(3): A loss of main propulsion, primary steering, or any associated component or control system that reduces the maneuverability of the vessel;
Interpreted as an occurrence where an applicable system or component unexpectedly fails, shuts downs, or is otherwise rendered unable to perform its specified function, no matter its duration, even if momentary.
It also includes any situation where an applicable system or component is required to be intentionally shut down as a casualty control measure.
Does not include scheduled, preventative maintenance or taking engines out of operation that are otherwise fully operational for fuel cost savings purposes.

## Slide 17: 46 CFR 4.05-1(a)(3): A loss of main propulsion, primary steering, or any associated component or control system that reduces the maneuverability of the vessel;
Broadly defined: main propulsion equipment (propeller, jets, prime mover, reduction gear, or any other mechanical equipment required to make any portion of main propulsion operate), primary steering equipment (electronics, rudders, pods, pumps, hydraulics, etc.), and associated components and control systems (helm controls, engine room controls, etc.).
Other systems are included if they are integral to safe vessel maneuverability. Failure of a system that reduces maneuverability of the vessel is a reportable casualty.
Redundancies that perform as designed may eliminate the need to report the casualty if the vessel does not experience a loss in maneuverability as defined in the next paragraph.

## Slide 18: 46 CFR 4.05-1(a)(3): A loss of main propulsion, primary steering, or any associated component or control system that reduces the maneuverability of the vessel;
an occurrence that renders a vessel incapable of maintaining safe speed and steerage for the prevailing or anticipated conditions (e.g., weather, other vessel traffic, tidal influences)
Or adversely impacts specific vessel operations (e.g., mooring, towing, anchoring, and dynamic positioning).

## Slide 19: 46 CFR 4.05-1(a)(4): An occurrence materially and adversely affecting the vessel’s seaworthiness or fitness for service or route….
Materially and adversely – A physical condition of the vessel or its associated equipment at a given point and time that requires remedial actions to circumvent, work around, or adapt operations as a result of an occurrence are considered to meet this condition.
Seaworthiness – Defined as the condition of being properly equipped, sufficiently constructed, and watertight in order to withstand stress of the wind, waves, and other environmental conditions that the vessel might reasonably be expected to encounter.

## Slide 20: 46 CFR 4.05-1(a)(4): An occurrence materially and adversely affecting the vessel’s seaworthiness or fitness for service or route….
Examples given: including but not limited to fire, flooding, or failure of or damage to fixed fire-extinguishing systems, lifesaving equipment, auxiliary power-generating equipment, or bilge-pumping systems

## Slide 21: 46 CFR 4.05-1(a)(4): An occurrence materially and adversely affecting the vessel’s seaworthiness or fitness for service or route….
Defined as the condition of the vessel and its equipment being such that it meets or exceeds minimum safety standards and is safe and reliable to operate in one or more particular types of service and in the locations in which it will be used.
Should an occurrence result in the material condition on the vessel becoming such that it requires the temporary or permanent reduction or restriction in the vessel’s operating parameters or route as compared to what it is permitted in its COI, then the occurrence is considered to have met this criterion.

## Slide 22: 46 CFR 4.05-1(a)(5): A loss of life
Includes “presumed lost/dead”
Any loss of life, regardless of the apparent cause (i.e. fatal heart attack)

## Slide 23: 46 CFR 4.05-1(a)(6): An injury that requires professional medical treatment (treatment beyond first aid) and, if the person is engaged or employed on board a vessel in commercial service, that renders the individual unfit to perform his or her routine duties;
Interpreted as damage or harm caused to the structure or function of the body as a result of an outside physical agent or force to a passenger, crewmember, or non-crewmember.
This includes injuries that occur due to criminal or intentional acts
Does not include illness
Does include injury caused by illness

## Slide 24: 46 CFR 4.05-1(a)(6): An injury that requires professional medical treatment (treatment beyond first aid) and, if the person is engaged or employed on board a vessel in commercial service, that renders the individual unfit to perform his or her routine duties;
Medical treatment does not include diagnostic testing or first aid
14 examples of first aid are given

## Slide 25: 46 CFR 4.05-1(a)(6): An injury that requires professional medical treatment (treatment beyond first aid) and, if the person is engaged or employed on board a vessel in commercial service, that renders the individual unfit to perform his or her routine duties;
Unfit to perform his or her routine duties –injuries that prevent a crew member from performing his or her normally assigned duties
Engaged or employed on board a vessel – includes individuals who are on board a vessel to carry out work associated with shipboard operations, cargo operations, or maintenance. Examples include pilots, accommodation and hospitality staff, “temporary workers” such as visiting technicians, riding crews, contractors, divers, personnel in support of commercial diving operations, and persons supporting Outer Continental Shelf activities.

## Slide 26: 46 CFR 4.05-1(a)(6): An injury that requires professional medical treatment (treatment beyond first aid) and, if the person is engaged or employed on board a vessel in commercial service, that renders the individual unfit to perform his or her routine duties;
46 CFR 4.01-3(c): Vessels are excluded from the requirements of § 4.05–1(a)(5) and (a)(6) with respect to the death or injury of shipyard or harbor workers when such accidents are not the result of either a vessel casualty (e.g., collision) or a vessel equipment casualty (e.g., cargo boom failure) and are subject to the reporting requirements of Occupational Safety and Health Administration (OSHA) under 29 CFR 1904
Guidance: As defined in Federal statutes and regulations, stevedores and longshoremen are not shipyard or harbor workers. However, for the purposes of applying this exclusion, the Coast Guard will consider incidents involving the death or injury of a stevedore or longshoremen…as equivalent to one involving a shipyard or harbor worker

## Slide 27: 46 CFR 4.05-1(a)(7): An occurrence causing property damage in excess of $25,000, this damage including the cost of labor and material to restore the property to its condition before the occurrence, but not including the cost of salvage, cleaning, gas-freeing, dry-docking, or demurrage
Property Damage – defined as the sum of the monetary cost of material damage of all property affected by the occurrence including, but not limited to vessels, cargos, facilities, aids-to-navigation, and bridges and their fendering systems.
Cargo-related damage estimates should be based solely on the loss or damage to the actual cargo; does not include demurrage or expenses related to storage or alternate delivery arrangements

## Slide 28: 46 CFR 4.05-1(a)(8): An occurrence involving significant harm to the environment as defined in 46 CFR 4.03-65.
Reporting requirements are found in 4.03-65; which in turn incorporates 40 CFR 110.3 and 40 CFR Part 117
Only guidance is that the reporting requirement applies only to discharges from commercial vessels (with the exception of state numbered commercial vessels that are not subject to inspection under 33 U.S.C. 3301); it does NOT include discharges from facilities, fixed platforms, non-vessels, or to mystery spills.